## Slide 1: Cortex-M4 Bare-Metal C Programming (nRF52840)
한동대학교
마이크로프로세서응용

## Slide 2: Agenda
Bare-metal C programming
Exercise1
Exercise2
Exercise3
Assignment

## Slide 3: What is Bare-Metal Programming ?
A Bare Metal embedded system is one where the application software runs directly on the hardware without the use of an operating system.
  Developers have full control over the hardware resources and
  must manage all aspects of the system themselves.

## Slide 4: in-line assembly
Embed assembly language code into C programs.
May be used for manually optimizing time critical parts of the software
or to use specific processor instruction, which are not available in the C language
Syntax in ARMCC:
__asm [volatile] ( assembly code in double quote )
__asm volatile ( “ADD R1,R2,R3”);
  The volatile qualifier disables certain compiler optimizations, which might otherwise lead to the compiler removing the code block.
  The volatile qualifier is optional, but you should consider using it around your assembly code blocks to ensure the compiler does not remove them when compiling with -O1 or higher
  Multiple Instructions within a __asm
void Function(void)
{
__asm (
"TST LR, #0x40\n\t"
"BEQ from_nonsecure\n\t"
"from_secure:\n\t"
"TST LR, #0x04\n\t"
"ITE EQ\n\t"
"MRSEQ R0, MSP\n\t“);
}

## Slide 5: volatile
C Keyword “volatile”
The declaration of a variable as volatile tells the compiler that the variable can be modified at any time externally to the implementation, for example, by the operating system, by another thread of execution such as an interrupt routine or signal handler, or by hardware.
To avoid optimization problems caused by changes to program state external to the implementation, you must declare variables as volatile whenever their values can change unexpectedly in ways unknown to the implementation.
In practice, you must declare a variable as volatile whenever you are:
  Accessing memory-mapped peripherals.
  Sharing global variables between multiple threads.
  Accessing global variables in an interrupt routine or signal handler.
The compiler does not optimize the variables you have declared as volatile.

## Slide 6: Agenda
Bare-metal programming
Exercise1
Exercise2
Exercise3
Assignment

## Slide 7: Exercise1
Translate the LED Blinking in Assembly Code into C using in-line assembly.
in-line assembly code
volatile keyword
  means “do not optimize with compiler”

## Slide 8: Exercise1
#include <stdint.h>
void volatile TURN_ON_LED()
{
__asm volatile(
"LDR R0, =0x50000504\n\t”
"LDR R1, =0x00002000\n\t"
"MVN R1, R1\n\t"
"STR R1, [R0]\n\t"
"MOV PC, LR\n\t"
);
}
void volatile Delay_loop()
{
__asm volatile(
"LDR R2, =16000000\n\t"
"count_down: CMP R2, #0\n\t"
"ITT NE\n\t"
"SUBNE R2, R2, #1\n\t"
"BNE count_down\n\t"
"MOV PC, LR\n\t"
);
}

## Slide 9: Exercise1
void volatile TURN_OFF_LED()
{
__asm(
"LDR R0, =0x50000504\n\t" // OUT register (for my board LED, 0:ON, 1:OFF)
"LDR R1, =0x00002000\n\t"
"STR R1, [R0]\n\t"
"MOV PC, LR\n\t"
);
}
void volatile SETTING()
{
__asm(
"LDR R0, = 0x50000000\n\t"
"LDR R1, =0x00008000\n\t"
"STR R1, [R0, 0x514]\n\t");
}
int main()
{
SETTING();
while(1)
{
TURN_ON_LED();
Delay_loop();
TURN_OFF_LED();
Delay_loop();
}
return 0;
}
Notes: 빌드를 하고 go를 하는데 빌드를 하 ㄹ대도, 내가 이전에 빌드했던 것을 클린하고 빌드를 누르는 설명이 있어야 함.(리빌드 솔루션). 그냥 go를 누르기 보다는 그 과정을 알려줘라. 릴리즈 모드는 뭐임?
디버거는 개발 단게에 있는 것임. 한 줄 한 줄 볼 수 있어야 해서 압축 하면 안되고 날 것의 그대로를가 ㅕ쟈함.
릴리즈는 디버거보다 더욱 최적화 되어 있는 프로그램. 한 줄 한 줄 볼 필요가 없어서 가벼워지고 빨리짐

## Slide 10: Agenda
Bare-metal programming
Exercise1
Exercise2
Exercise3
Assignment

## Slide 11: Exercise2
Implement a code that blinks LED3 in C.

## Slide 12: Exercise2
#include <stdint.h>
#define LED1_MASK 0x00002000
#define LED2_MASK 0x00004000
#define LED3_MASK 0x00008000
#define LED4_MASK 0x00010000
#define LED_ALL_MASK (LED1_MASK+LED2_MASK+LED3_MASK+LED4_MASK)
#define GPIO_P0_BASE 0x50000000
#define GPIO_OUT_REG_OFFSET 0x0504
#define GPIO_DIR_REG_OFFSET 0x0514
#define GPIO_DIRSET_REG_OFFSET 0x0518
void volatile setting()
{
volatile uint 32_t *dir_reg =
(uint32_t*)(GPIO_P0_BASE+GPIO_DIR_REG_OFFSET);
*dir_reg = LED3_MASK;
}
void volatile turn_OFF_LED()
{
volatile uint32_t * out_reg =
(uint32_t *)(GPIO_P0_BASE+GPIO_OUT_REG_OFFSET);
*out_reg = LED3_MASK;
}
void volatile turn_ON_LED()
{
volatile uint32_t *out_reg =
(uint32_t *)(GPIO_P0_BASE+GPIO_OUT_REG_OFFSET);
*out_reg = ~LED3_MASK;
}
int main()
{
setting();
while(1) {
turn_ON_LED();
delay_loop();
turn_OFF_LED();
delay_loop();
}
return 0;
}

## Slide 13: Exercise2
void volatile delay_loop()
{
__asm(
"LDR R2, =16000000\n\t"
"count_down: CMP R2, #0\n\t"
"ITT NE\n\t"
"SUBNE R2, R2, #1\n\t"
"BNE count_down\n\t"
"MOV PC, LR\n\t"
);
//for(int i = 6400000; i >0; i--);
}

## Slide 14: Agenda
Bare-metal programming
Exercise1
Exercise2
Exercise3
Assignment

## Slide 15: Exercise3
Use Polling method to check Button Push in C.
If button1 push -> Led3 toggle

## Slide 16: Exercise3
#include <stdint.h>
#define LED1_MASK 0x00002000
#define LED2_MASK 0x00004000
#define LED3_MASK 0x00008000
#define LED4_MASK 0x00010000
#define GPIO_P0_BASE 0x50000000
#define GPIO_OUT_REG_OFFSET 0x0504
#define GPIO_DIR_REG_OFFSET 0x0514
#define GPIO_DIRSET_REG_OFFSET 0x0518
#define GPIO_IN_REG_OFFSET 0x510
#define BTN1_MASK 0x00800
#define BTN2_MASK 0x01000
#define GPIO_PIN_CNF_11_OFFSET 0x72C
void volatile TURN_ON_LED()
{
volatile uint32_t *OUT_REG = (uint32_t *)(GPIO_P0_BASE+GPIO_OUT_REG_OFFSET);
*OUT_REG = ~LED3_MASK;
}
void volatile Delay_loop()
{
__asm(
"LDR R2, =1600000\n\t"
"count_down: CMP R2, #0\n\t"
"ITT NE\n\t"
"SUBNE R2, R2, #1\n\t"
"BNE count_down\n\t"
"MOV PC, LR\n\t"
);
//for(int i = 6400000; i >0; i--);
}

## Slide 17: Exercise3
void volatile TURN_OFF_LED()
{
volatile uint32_t *OUT_REG = (uint32_t *)(GPIO_P0_BASE+GPIO_OUT_REG_OFFSET);
*OUT_REG = LED3_MASK;
}
void volatile SETTING()
{
*((uint32_t*)(GPIO_P0_BASE+GPIO_DIR_REG_OFFSET)) = LED3_MASK;
*((uint32_t*)(GPIO_P0_BASE+GPIO_PIN_CNF_11_OFFSET)) = 0x0003000c;
}
void volatile WAIT_INPUT_PUSH()
{
while(1)
{
volatile uint32_t button_state = *((uint32_t*)(GPIO_P0_BASE+GPIO_IN_REG_OFFSET));
button_state = ~button_state;
if(button_state & BTN1_MASK)
break;
}
}

## Slide 18: Exercise3
int main()
{
SETTING();
while(1)
{
TURN_ON_LED();
Delay_loop();
WAIT_INPUT_PUSH();
TURN_OFF_LED();
Delay_loop();
WAIT_INPUT_PUSH();
}
return 0;
}

## Slide 19: Agenda
Bare-metal programming
Exercise1
Exercise2
Exercise3
Assignment

## Slide 20: Assignment
Write a bare-metal C program to change LED 1 and LED 2 for every button 1 push event such as (LED1, LED2) = (0,1)  (1,0)  (1,1)  (0,0)  (0,1)  …
// init, unsigned 1 byte of memory -> check docs to see if uint32_t is more efficient
unsigned char curr_led_state = 0b00;
// per-iter, add the value of 1, reset to 0b00 if over 0b11
curr_led_state = curr_led_state + 1;
if (curr_led_state > 0b11) { curr_led_state = 0b00; }
// match led_mask with curr_led_state
// LED1 = 0b0…01…0, LED2 = 0b0…10…0, << 13 bits (LED_MASK_SHFT)
LED_MASK = curr_led_state << LED_MASK_SHFT;
// write to outclr – 1 must be on
*outclr_reg = LED_MASK;
Notes: 빌드를 하고 go를 하는데 빌드를 하 ㄹ대도, 내가 이전에 빌드했던 것을 클린하고 빌드를 누르는 설명이 있어야 함.(리빌드 솔루션). 그냥 go를 누르기 보다는 그 과정을 알려줘라. 릴리즈 모드는 뭐임?
디버거는 개발 단게에 있는 것임. 한 줄 한 줄 볼 수 있어야 해서 압축 하면 안되고 날 것의 그대로를가 ㅕ쟈함.
릴리즈는 디버거보다 더욱 최적화 되어 있는 프로그램. 한 줄 한 줄 볼 필요가 없어서 가벼워지고 빨리짐