## Slide 1: ARM ASSEMBLY programming Practice (1)
한동대학교-
마이크로프로세서응용

## Slide 2: UAL: Unified Assembly Language
UAL stands for Unified Assembly Language, which is a syntax standard for writing assembly language code for ARM processors.
UAL was introduced with the ARMv7 architecture to provide a consistent assembly language interface, accommodating both the ARM and Thumb instruction sets.
It provides a unified approach, whether you're targeting a 32-bit ARM instruction, a 16-bit Thumb instruction, or the newer 32-bit Thumb-2 extensions.

## Slide 3: Assembler Structure
Each line of assembly language source code form:
{label} {instruction|directive|pseudo-instruction} {;comment}
label
  is a address symbol
  In some directives it is a symbol for a variable (address) or a constant
  must begin in the first column
  optional
directive
  provides important information to the assembler
  similar to C compiler directives
instruction and pseudo instruction must begin with white space

## Slide 4: UAL Syntax
Operator: Instruction Mnemonics such as ADD for addition, MOV for move
Conditional Codes: optional inclusion of condition code with instructions enabling conditionl execution.
  is a suffix attached to the instruction mnemonics like EQ(equal), NE(not equal), GT*greater)
  Ex) ADDEQ, ADDNE, ADDGT
    compared with zero, [X0]
Operands(registers): Rn (n = 0,…, 15) or PC, SP, LR for special register
Operands(immediate): prefix # and value like #16 (decimal 16), #0x1F (hexa 1F),
Operands(memory access): use brackets like [R1]
Operands(Shift and Rotate): LSL #2 (shift left 2bit), ROR #2 (rotate 2 bits)
Labels: marking positions in code (symbol for address)

## Slide 5: Assembler Directives
Directive | Meaning | Example | Note
DCD | Define Constant Double (32bits) | DAT DCD d1, d2, d3, …, dn | in data memory set next n words to numeric value given by d1, d2, … dn
DCB | Define Constant Byte (8bit) | DAT2 DCB d1, d2, …, dn | in data memory set next n bytes to numeric value given by d1, d2, … dn n must be dividable by 4 Bytes are written in Little-endian order
FILL | Fill the space (#words) | DAT3 FILL 40 | Fill next 40 words of data memory with zero
ADR | Address | ADR Ra, Label | Set Ra egister as Label Same as MOV Ra, #Label but literal values closer to PC are allowed
EQU | Equals | LAB2 EQU LABEL+1 | Sets its label (LAB2) equal to given numeric expression (LABEL+4)

## Slide 6: Assembler program sample
- What is wrong with the example?
Hint: Look at the immediate values and loading 32-bit constants in the ARM Programming Techniques document.]
ENTRY ; mark first instruction
start
MOV r0, #0x1 ; = 1
MOV r1, #0xFFFFFFFF ; = -1 (signed)
MOV r2, #0xFF ; = 255
MOV r3, #0x101 ; = 257
MOV r4, #0x400 ; = 1024
stop
END ; Mark end of file
ENTRY ; mark first instruction
start
MOV r0, #0x1 ; = 1
LDR r1, =const
MOV r2, #0xFF ; = 255
MOV r3, #0x101 ; = 257
MOV r4, #0x400 ; = 1024
stop ; Terminate
const
DBC
END ; Mark end of file

## Slide 7: ARM Assembler Lab Environment Settings
Web-based ARM Assembler Simulator
  CPUlator from Altera FPGA (Intel)
  https://cpulator.01xz.net/?sys=arm
Stand-alone programs
  Keil uVision from ARM
  visUAL
  Embedded Studio from Segger
  VS Code with nRF Connect Extension from Nordic

## Slide 8: visUAL2
https://github.com/tomcl/V2releases/releases

## Slide 9: Data Movement (Immediate to Register, Register to Register)
start
MOV r0, #128
MOV r1, #0xF0
MOV r2, #0xFA
MOV r1, #0x7F00
MVN r1, #0xF0
MVN r1, #0xA5
MOV r6, r2
MVN r6, r6
instruction | r0 | r1 | r2 | r6
initial value | 0x0 | 0x0 | 0x0 | 0x0
after MOV r0, #128 | 0x80 | 0x0 | 0x0 | 0x0
after MOV r1, #0xF0 | 0x80 | 0xF0 | 0x0 | 0x0
after MOV r2, #0xFA | 0x80 | 0xF0 | 0xFA | 0x0
after MOV r1, #0x7F00 | 0x80 | 0x7F00 | 0xFA | 0x0
after MVN r1, #0xF0 | 0x80 | 0xFFFFFF0F | 0xFA | 0x0
after MOV r6, r2 | 0x80 | 0xFFFFFF5A | 0xFA | 0xFA
MVN r6, r6 | 0x80 | 0xFFFFFF5A | 0xFA | 0xFFFFFF05

## Slide 10: Data Movement (Shifted data)
start
MOV r0, #0xA7
MOV r1, r0, LSL #1
MOV r1, r0, LSL #4
MVN r2, r1
MOV r1, r2, LSR #1
MOV r1, r2, ASR #1
MOV r2, r2, ROR #1
MVN r3, r0, ROR #2 stop END
instruction | r0 | r1 | r2 | r3
initial value | 0x0 | 0x0 | 0x0 | 0x0
after MOV r0, #0xA7 | 0xA7 | 0x0 | 0x0 | 0x0
after MOV r1, r0, LSL #1 | 0xA7 | 0x14E | 0x0 | 0x0
after MOV r1, r0, LSL #4 | 0xA7 | 0xA70 | 0x0 | 0x0
after MVN r2, r1 | 0xA7 | 0xA70 | 0xFFFFF58F | 0x0
after MOV r1, r2, LSR #1 | 0xA7 | 0x7FFFFAC7 | 0xFFFFF58F | 0x0
after MOV r1, r2, ASR #1 | 0xA7 | 0xFFFFFAC7 | 0xFFFFF58F | 0x0
after MOV r2, r2, ROR #1 | 0xA7 | 0xFFFFFAC7 | 0xFFFFFAC7 | 0x0
after MVN r3, r0, ROR #2 | 0xA7 | 0xFFFFFAC7 | 0xFFFFFAC7 | 0x3FFFFFD6

## Slide 11: Data Movement (Memory word to Register)
Test various Load instructions
by executing the assembly code
Explain the differences of addressing modes with LDR
_start
LDR R0,=0x00ff
LDR R1,=list
MOV R2, #4
LDR R0, [R1], #4
LDR R0, [R1,R2]
LDR R0, [R1,R2]!
LDR R0, [R1], R2
LDR R0, [R1, #4]
LDR R0, [R1, #4]!
LDR R0, [R1, R2, LSL #1]
LDR R0, [R1, R2, LSL #1]!
stop B stop
list
DCD 9,8,7,6,5,4,3,2,1,10,11,12,-1,-2
9
8
7
6
5
4
3
2
1
000000ff
list:
R0:
R1:
R2:
00000038
00000004
registers
Memory

## Slide 12: 실습문제 (LDR: Memory to Register)
Complete the Table and Explain the reason for each register value change before vs. after
Instructions | 실행전 R0 | 실행후 R0 | 실행전 R1 | 실행 후 R1 | 실행 전 R2 | 실행 후 R2
LDR R0, [R1] | 0xFF | 0x9 | 0x200 | 0x200 | 0x4 | 0x4
LDR R0, [R1], #4 | 0x9 | 0x9 | 0x200 | 0x204 | 0x4 | 0x4
LDR R0, [R1,R2] | 0x9 | 0x7 | 0x204 | 0x204 | 0x4 | 0x4
LDR R0, [R1,R2]! | 0x7 | 0x7 | 0x204 | 0x208 | 0x4 | 0x4
LDR R0, [R1], R2 | 0x7 | 0x7 | 0x208 | 0x20C | 0x4 | 0x4
LDR R0, [R1, #4] | 0x7 | 0x5 | 0x20C | 0x20C | 0x4 | 0x4
LDR R0, [R1, #4]! | 0x5 | 0x5 | 0x20C | 0x210 | 0x4 | 0x4
LDR R0, [R1, R2, LSL #1] | 0x5 | 0x3 | 0x210 | 0x210 | 0x4 | 0x4
LDR R0, [R1, R2, LSL #1]! | 0x3 | 0x3 | 0x210 | 0x218 | 0x4 | 0x4
2. Change the first assembly code into “LDR R0, =0xffff” and compile and Run the code. Find the difference(s) and Explain the reason if any.
Modifying R0 to 0xffff simply changes the initial value of R0 from 0xFF to 0xFFFF, but other values are the same. This is because the next instruction overwrites R0 by loading from [R1].

## Slide 13: Data Movement (Register to Memory word)
Test various Store instructions by executing the assembly code
Explain the differences of addressing modes with STR
strat
LDR R0,=0x00ff
LDR R1,=list
MOV R2, #4
STR R0, [R1]
STR R0, [R1], #4
STR R0, [R1,R2]
STR R0, [R1,R2]!
STR R0, [R1], R2
STR R0, [R1, #4]
STR R0, [R1, #4]!
STR R0, [R1, R2, LSL #1]
STR R0, [R1, R2, LSL #1]!
loop B loop
list DCD 9,8,7,6,5,4,3,2,1,10,11,12,-1,-2
9
8
7
6
5
4
3
2
1
000000ff
list:
R0:
R1:
R2:
00000038
00000004
registers
Memory

## Slide 14: 실습문제 (STR: Register to Memory)
Complete the Table
Show the memory Contents after execution of each instruction
Instructions | 실행전 R0 | 실행후 R0 | 실행전 R1 | 실행 후 R1 | 실행 전 R2 | 실행 후 R2 | list | list+4 | list+8 | list+C | list+10 | list+14 | list+18 | list+1C
STR R0, [R1] | 0xFF | 0xFF | 0x200 | 0x200 | 0x4 | 0x4 | 0xFF | 0x8 | 0x7 | 0x6 | 0x5 | 0x4 | 0x3 | 0x2
STR R0, [R1], #4 | 0xFF | 0xFF | 0x200 | 0x204 | 0x4 | 0x4 | 0xFF | 0x8 | 0x7 | 0x6 | 0x5 | 0x4 | 0x3 | 0x2
STR R0, [R1,R2] | 0xFF | 0xFF | 0x204 | 0x204 | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0x5 | 0x4 | 0x3 | 0x2
STR R0, [R1,R2]! | 0xFF | 0xFF | 0x204 | 0x208 | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0x5 | 0x4 | 0x3 | 0x2
STR R0, [R1], R2 | 0xFF | 0xFF | 0x208 | 0x20C | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0x5 | 0x4 | 0x3 | 0x2
STR R0, [R1, #4] | 0xFF | 0xFF | 0x20C | 0x20C | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0xFF | 0x4 | 0x3 | 0x2
STR R0, [R1, #4]! | 0xFF | 0xFF | 0x20C | 0x210 | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0xFF | 0x4 | 0x3 | 0x2
STR R0, [R1, R2, LSL #1] | 0xFF | 0xFF | 0x210 | 0x210 | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0xFF | 0x4 | 0xFF | 0x2
STR R0, [R1, R2, LSL #1]! | 0xFF | 0xFF | 0x210 | 0x218 | 0x4 | 0x4 | 0xFF | 0x8 | 0xFF | 0x6 | 0xFF | 0x4 | 0xFF | 0x2

## Slide 15: Data Movement (Byte Load/Store, Little-Endian)
Draw Memory Contents
start LDR r9, =data
LDR r10,=data2
LDR r0, [r9]
LDR r1, [r9,#4]
STR r1, [r10]
LDRB r0, [r9]
LDRB r1, [r9, #1]
LDR r0,=0x11223344
LDR r1,=0xFFEEDDCC
STRB r0, [r10]
STRB r1, [r10,#1]
stop END
data DCB 0xA0, 0x11, 0x22, 0x33
DCD 0x44556677 data2 Fill 16
address | contents (byte) |  |  | 
 | initial | after 1st STR | STRB r0,.. | STRB r1, …
data | 0xA0 | 0xA0 | 0xA0 | 0xA0
data+1 | 0x11 | 0x11 | 0x11 | 0x11
data+2 | 0x22 | 0x22 | 0x22 | 0x22
data+3 | 0x33 | 0x33 | 0x33 | 0x33
data+4 | 0x77 | 0x77 | 0x77 | 0x77
data+5 | 0x66 | 0x66 | 0x66 | 0x66
data+6 | 0x55 | 0x55 | 0x55 | 0x55
data+7 | 0x44 | 0x44 | 0x44 | 0x44
data2 | 0x0 | 0x77 | 0x44 | 0x44
datas+1 | 0x0 | 0x66 | 0x66 | 0xCC
data2+2 | 0x0 | 0x55 | 0x55 | 0x55
data2+3 | 0x0 | 0x44 | 0x44 | 0x44

## Slide 16: Data Movement (multiple Memory word to Registers )
Execute the assembly program
start
LDR r0, =0xDDCCEE11
LDR r1, =0x22EEFF11
MOV r2, #0xAA00 ; 8bit constant with shift
MOV r3, #0xBB00 ; 8bit constant with shift
MOV r4, #0xCC00 ; 8bit constant with shift
MOV r5, #0xDD00 ; 8bit constant with shift
LDR r9, =table2
LDR r10,=destination
LDMDA r9, {r0,r1,r2}
STMDA r10, {r3,r4,r5}
LDMDB r9!, {r0-r2}
STMDB r10!, {r3-r5}
END
table DCD 0x00112233
DCD 0x1111AAAA
DCD 0xFF224488
DCD 0x44556677
table2 DCD 0x08090A0B
DCD 0x2222BBBB
DCD 0x3333CCCC
DCD 0x4444EEEE
destination Fill 16

## Slide 17: 실습문제 (LDMDA, STMDA, LDMDB, STMDB)
Complete the Table
Instructions | 실행전 r0,r1,r2 | 실행후 r0,r1,r2 | 실행전 r3,r4,r5 | 실행 후 r3,r4,r5 | 실행 전 r9,r10 | 실행 후 r9,r10
LDR r9, =table2 | 0xDDCCEE11, 0x22EEFF11, 0xAA00 | 0xDDCCEE11, 0x22EEFF11, 0xAA00 | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x0, 0x0 | 0x210, 0x0
LDR r10,=destination | 0xDDCCEE11, 0x22EEFF11, 0xAA00 | 0xDDCCEE11, 0x22EEFF11, 0xAA00 | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x210, 0x0 | 0x210, 0x220
LDMDA r9,{r0,r1,r2} | 0xDDCCEE11, 0x22EEFF11, 0xAA00 | 0xFF224488, 0x44556677, 0x8090A0B | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x210, 0x220 | 0x210, 0x220
STMDA r10, {r3,r4,r5} | 0xFF224488, 0x44556677, 0x8090A0B | 0xFF224488, 0x44556677, 0x8090A0B | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x210, 0x220 | 0x210, 0x220
LDMDB r9!, {r0-r2} | 0xFF224488, 0x44556677, 0x8090A0B | 0x1111AAAA, 0xFF224488, 0x44556677 | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x210, 0x220 | 0x204, 0x220
STMDB r10!, {r3-r5} | 0x1111AAAA, 0xFF224488, 0x44556677 | 0x1111AAAA, 0xFF224488, 0x44556677 | 0xBB00, 0xCC00, 0xDD00 | 0xBB00, 0xCC00, 0xDD00 | 0x204, 0x220 | 0x204, 0x214

## Slide 18: Exercise-1: Load and Store
;AREA ArrayIteration, CODE, READONLY
ENTRY
LDR R0, =sourceArray ; Base address of the source array
LDR R1, =destinationArray ; Base address of the destination array
MOV R4, #10 ; Counter for the number of elements to process
loop
; TODO (1) : Load from source array using pre-indexed addressing
; TODO (2) : Modify loaded value by incementing 1
; TODO (3) : Store to destination array using post-indexed addressing
; Decrement the counter and loop until done
SUBS R4, R4, #1
BNE loop
END
Implement the loading of an integer from the sourceArray using pre-indexed addressing. The syntax for pre-indexed LDR with an immediate offset
After modifying the loaded value (incrementing in the given operation),
store it into the destinationArray using post-indexed addressing.

## Slide 19: Exercise-1 Answer
;AREA ArrayIteration, CODE, READONLY
ENTRY
LDR R0, =sourceArray ; Base address of the source array
LDR R1, =destinationArray ; Base address of the destination array
MOV R4, #10 ; Counter for the number of elements to process
SUB R0, R0, #4
loop
LDR R2, [R0, #4]!
ADD R2, R2, #1
STR R2, [R1], #4
SUBS R4, R4, #1
BNE loop
END

## Slide 20: Exercise-2: Multiple Data Load and Store
Modify the Exercise-1 using multiple word load and store
load two words at a time using LDM
store two words at a time using STM

## Slide 21: Exercise-2 Ans
;AREA ArrayIteration, CODE, READONLY
ENTRY
LDR R0, =sourceArray ; Base address of the source array
LDR R1, =destinationArray ; Base address of the destination array
MOV R4, #10 ; Counter for the number of elements to process
LSR R4, R4, #1
loop
LDMIA R0!, {R2, R3}
ADD R2, R2, #1
ADD R3, R3, #1
STMIA R1!, {R2, R3}
SUBS R4, R4, #1
BNE loop
END

## Slide 22: Exercise 2-2 Multiple data load/store(2)
Objective: (1) Load multiple pieces of data from memory into registers,
(2) modify this data (increment), and then (3) store the modified data back into memory.
Initial Setup
  Assume that there are four consecutive words (32-bit) of data stored in memory. For example, starting at address 0x00001000 to 0x0000100C, the values 1, 2, 3, 4 are stored respectively.
Goal 1: Load Data from Memory into Registers
  Use the LDM instruction to load the four words of data from the previously defined memory address into registers R0 to R3 consecutively.
Modify Data
  Perform different operations on the loaded data. For example, increment R0 and R1 by 1, and R2 and R3 by 2.
Goal 2: Store Data from Registers back into Memory
  Use the STM instruction to store the modified data from R0 to R3 back into a new location in memory. For instance, start storing at address 0x20002000

## Slide 23: Ans.
AREA Reset, DATA, READWRITE ; Define initial data
DCD 1, 2, 3, 4 ; Assume this is located at address 0x20001000
AREA Reset, CODE, READONLY
ENTRY
; Use LDM to load data into R0-R3
LDR R4, =0x20001000 ; Load start address into R4
LDMIA R4!, {R0-R3} ; Load data from memory into R0-R3
; Modify data
ADD R0, R0, #1
ADD R1, R1, #1
ADD R2, R2, #2
ADD R3, R3, #2
; Use STM to store data back into memory
LDR R4, =0x20002000 ; Load new start address into R4
STMIA R4!, {R0-R3} ; Store data from R0-R3 back into memory
END

## Slide 24: Data Processing Instructions
Arithmetic (integer) and Bitwise logic Operations
General Rules:
  All operands are 32-bits coming from registers or literals
  The results, if any, is 32-bits and placed in a register (with exception for long multiply which produces a 64-bit result)
  3 address format

## Slide 25: Arithmetic Operation (1)
ADD: ADD two numbers (r3+r4)
ADDS : ADD two numbers and accordingly change the CPSR (process status) based on the result (r3+r4  NZCV)
ADC : Add with carry (r3+r4+C)
SUB : Subtract two numbers (r3-r4)
SUBS: Subtract two numbers and accordingly change the CPSR (process status) based on the result (r3-r4  NZCV)
SUC : Subtract with borrow (r3-r4-1+C)
RSB : Reverse subtract (r4-r3)
RSC : r4-r3-1+C
.global _start
_start:
MOV R5, #F
MOV R6 #8
MOV R3, #0xF0000000
MOV R4, #0x60000000
ADD R5, R3,R4
ADDS R5,R3,R4
ADC R6,R3,R4
SUB R5, R3, R4
SUBS R5,R3,R4
SBC R6,R3,R4
RSBS R5,R3,#0x01
RSC R6,R3,#0x01
MOV R3, #5
ADD R5, R3, R3, LSL #2 ; r5=5*r3
RSB R6, R5, R5, LSL #3; r10=7*r9

## Slide 26: Arithmetic Operation (2)
 | R3 | R4 | R5 (After) | R6(After) | CPSR(Before) | CPSR(After)
ADD R5,R3,R4 |  |  |  |  |  | 
ADDS R5,R3,R4 |  |  |  |  |  | 
ADC R6,R3,R4 |  |  |  |  |  | 
SUBS R5,R3,R4 |  |  |  |  |  | 
SBC R6,R3,R4 |  |  |  |  |  | 
RSB R5, R3, #1 |  |  |  |  |  | 
RSC R6, R3, #1 |  |  |  |  |  | 
ADD R5, R3, R3, LSL #2 |  |  |  |  |  | 
RSB R6, R5, R5, LSL #3 |  |  |  |  |  | 
Complete the table

## Slide 27: Arithmetic (Multiplication)
MUL Rd, Rn, Rm @multiply 32-bits
  Rd=Rn x Rm
  Second operand (Rm) cannot be immediate
  The result register must be different from the first operand
  If S bit is set, C flag is meaningless
MLA Rd, Rn, Rm Rs @ Multiply-accumulate
  Rd = RnxRm+Rs
Multiplying a constant can often be implemented with shifted register operand
  MOV R1, #35 + MUL R2, R0, R1
  vs.
  ADD R0, R0, R0 LSL #2 + RSB R2, R0, R0, LSL #3
.global _start
_start:
MOV R5, #000
MOV R3, #0x30
MOV R4, #0x50
MOV R6, #0x09
MULS R5, R3,R4
MLA R5, R3,R4,R6
 | R5(Before) | R5(After)
MUL R5,R3,R4 |  | 
MULA R5,R3,R4,R6 |  | 

## Slide 28: Bitwise Operation
AND Rd, Rn, Rm : Rd = Rn and Rm
ORR Rd, Rn, Rm : Rd = Rn or Rm
EOR Rd, Rn, Rm: Rd = Rn xor Rm
BIC Rd, Rn, Rm : bit clear
@ Rd = Rn and (~Rm)
.global _start
_start:
MOV R5, #0
MOV R3, #0x30
MOV R4, #0x50
AND R5, R3, R4
ORR R5, R3, R4
EOR R5, R3, R4
BIC R5, R3, R4
BIC R5, R3, #0x10
BIC R5, R3, #0x30
BICS R5, R3, #0x30

## Slide 29: Logical Operation(2)
Complete the table
 | R3(Before) | R4(Before) | R5 (Before) | R5(After) | CPSR(After)
AND R5,R3,R4 |  |  |  |  | 
ORR R5,R3,R4 |  |  |  |  | 
EOR R5,R3,R4 |  |  |  |  | 
BIC R5, R3, R4 |  |  |  |  | 
BIC R5,R3,#0x10 |  |  |  |  | 
BIC R5, R3, #0x30 |  |  |  |  | 
BICS R5, R3, #0x30 |  |  |  |  |