## Slide 1: ARM ASSEMBLY programming Practice (2)
한동대학교-
마이크로프로세서응용

## Slide 2: Data Processing Instructions
Arithmetic (integer) and Bitwise logic Operations
General Rules:
  All operands are 32-bits coming from registers or literals
  The results, if any, is 32-bits and placed in a register (with exception for long multiply which produces a 64-bit result)
  3 address format

## Slide 3: Arithmetic Operation (1)
ADD: ADD two numbers (r3+r4)
ADDS : ADD two numbers and accordingly change the CPSR (process status) based on the result (r3+r4  NZCV)
ADC : Add with carry (r3+r4+C)
SUB : Subtract two numbers (r3-r4)
SUBS: Subtract two numbers and accordingly change the CPSR (process status) based on the result (r3-r4  NZCV)
SUC : Subtract with borrow (r3-r4-1+C)
RSB : Reverse subtract (r4-r3)
RSC : r4-r3-1+C
.global _start
_start:
MOV R5, #F
MOV R6 #8
MOV R3, #0xF0000000
MOV R4, #0x60000000
ADD R5, R3,R4
ADDS R5,R3,R4
ADC R6,R3,R4
SUB R5, R3, R4
SUBS R5,R3,R4
SBC R6,R3,R4
RSBS R5,R3,#0x01
RSC R6,R3,#0x01
MOV R3, #5
ADD R5, R3, R3, LSL #2 ; r5=5*r3
RSB R6, R5, R5, LSL #3; r10=7*r9

## Slide 4: Arithmetic Operation (2)
 | R3 | R4 | R5 (After) | R6(After) | CPSR(Before) | CPSR(After)
ADD R5,R3,R4 |  |  |  |  |  | 
ADDS R5,R3,R4 |  |  |  |  |  | 
ADC R6,R3,R4 |  |  |  |  |  | 
SUBS R5,R3,R4 |  |  |  |  |  | 
SBC R6,R3,R4 |  |  |  |  |  | 
RSB R5, R3, #1 |  |  |  |  |  | 
RSC R6, R3, #1 |  |  |  |  |  | 
ADD R5, R3, R3, LSL #2 |  |  |  |  |  | 
RSB R6, R5, R5, LSL #3 |  |  |  |  |  | 
Complete the table

## Slide 5: Arithmetic (Multiplication)
MUL Rd, Rn, Rm @multiply 32-bits
  Rd=Rn x Rm
  Second operand (Rm) cannot be immediate
  The result register must be different from the first operand
  If S bit is set, C flag is meaningless
MLA Rd, Rn, Rm Rs @ Multiply-accumulate
  Rd = RnxRm+Rs
Multiplying a constant can often be implemented with shifted register operand
  MOV R1, #35 + MUL R2, R0, R1
  vs.
  ADD R0, R0, R0 LSL #2 + RSB R2, R0, R0, LSL #3
.global _start
_start:
MOV R5, #000
MOV R3, #0x30
MOV R4, #0x50
MOV R6, #0x09
MULS R5, R3,R4
MLA R5, R3,R4,R6
 | R5(Before) | R5(After)
MUL R5,R3,R4 |  | 
MULA R5,R3,R4,R6 |  | 

## Slide 6: Bitwise Operation
AND Rd, Rn, Rm : Rd = Rn and Rm
ORR Rd, Rn, Rm : Rd = Rn or Rm
EOR Rd, Rn, Rm: Rd = Rn xor Rm
BIC Rd, Rn, Rm : bit clear
@ Rd = Rn and (~Rm)
.global _start
_start:
MOV R5, #0
MOV R3, #0x30
MOV R4, #0x50
AND R5, R3, R4
ORR R5, R3, R4
EOR R5, R3, R4
BIC R5, R3, R4
BIC R5, R3, #0x10
BIC R5, R3, #0x30
BICS R5, R3, #0x30

## Slide 7: Logical Operation(2)
Complete the table
 | R3(Before) | R4(Before) | R5 (Before) | R5(After) | CPSR(After)
AND R5,R3,R4 |  |  |  |  | 
ORR R5,R3,R4 |  |  |  |  | 
EOR R5,R3,R4 |  |  |  |  | 
BIC R5, R3, R4 |  |  |  |  | 
BIC R5,R3,#0x10 |  |  |  |  | 
BIC R5, R3, #0x30 |  |  |  |  | 
BICS R5, R3, #0x30 |  |  |  |  |